## Slide 1
ELEMENTAL ANALYSIS
Fundamental Questions for an Analytical Chemist
  What is in the sample?
  How much is there?
What is the elemental composition?
[C, O, N, F, Cl, P, H, etc. ?]

## Slide 2
ELEMENTAL ANALYSIS
Chemical Methods
  Types of Analysis:
      Qualitative Analysis:
        Gives information only on whether or not a compound or element is present
        Often inexpensive, manual method
        Usually requires large amount of sample (mg-mg)
      Quantitative Analysis:
        Measures the exact amount of compound present in the sample
        Performed for a known sample
        Often requires high accuracy and precision
      Semi-Quantitative Analysis
        Identifies presence or absence of element or compound
        Provides some crude measure of the amount of compound present (i.e., screening method)

## Slide 3
Chemical Methods
  Qualitative Elemental Analysis by Chemical Methods:
      Generally based on characteristic reactions and properties of elements:
        Physical phase (solid/liquid/gas)
        Color/spectral properties (flame test)
        Solubility and volatility
        Precipitation, colored products, etc.
      Typically based on solution reactions:
        Sample is placed in a solution before the procedure can be performed
ELEMENTAL ANALYSIS
Flame test - metal ions produce characteristic color in a flame
Solubility test - an unknown black compound is partially dissolved in ethanol and acetone

## Slide 4
Chemical Methods
  Methods of Sample Preparation for Elemental Analysis:
      Simple sample dissolution:
        Water: Good for dissolving many inorganic compounds and some organic compounds. Slight amount of acid often added to prevent hydrolysis and precipitation of metal cations
        Organic solvents: Includes alcohols, chlorinated hydrocarbons, ketones, etc. Typically used to dissolve organic compounds for analysis
        Mineral acids: Includes nitric acid, hydrochloric acid, aqua regia, sulfuric acid, etc. Dissolves most metals, metal alloys, metal oxides, carbonates and sulfides.
ELEMENTAL ANALYSIS
Gold dissolved in aqua regia
[1:3 mixture of nitric acid and hydrochloric acid ]

## Slide 5
ELEMENTAL ANALYSIS
Group Separations in
Qualitative Analysis
Using Selective Precipitation

## Slide 6
Chemical Methods
  Methods of Sample Preparation for Elemental Analysis:
      II. Wet Ashing
        Treatment of sample with mixture of acids (i.e., perchloric and nitric acid) and heat.
        Acid acts to oxidize and dissolve sample
        Commonly used for elemental analysis of complex biological samples
        Problem: conditions may not be harsh enough for many elements.
      III. Dry Ashing:
        Treatment of sample to form a metal oxide or carbonate, which is then dissolved in dilute acid
        Used for elemental analysis of organic and many inorganic compounds
        Problem: Low recovery for volatile elements (C, O, H)
ELEMENTAL ANALYSIS
Ashing can be done with a furnace or microwave oven

## Slide 7
Chemical Methods
  Methods of Sample Preparation for Elemental Analysis:
      IV. Fusion:
        Convert sample to powder and heat in the presence of a high temperature acid (potassium pyrosulfate, K2S2O7), base (sodium carbonate, Na2CO3), or oxidizing agent (sodium peroxide, Na2O2) in a Pt or graphite crucible
        After cooling, this converts many metallic and non-metallic elements to ionic forms soluble in dilute HCl
        Commonly used in the elemental analysis of ore samples
        Problem: Low recovery for volatile elements (C, O, H). Can be dangerous to perform.
ELEMENTAL ANALYSIS

## Slide 8
Chemical Methods
  Specific Elemental Methods: Carbon and Hydrogen Analysis
      I. Combustion Analysis:
        Typically used to determine C and H content of pure compounds
        Based on burning the sample in the presence of excess oxygen, converting all C, H, N and S into volatile oxides:
        To get at O content, method may be modified by using F2 in place of O2 as the oxidizing agent:
        Problem: much more hazardous, difficult and expensive to do than normal combustion analysis with O2. Best performed by robots or automated systems.
ELEMENTAL ANALYSIS

## Slide 9
Chemical Methods
  Specific Elemental Methods: Carbon and Hydrogen Analysis
      II. Methods for Quantitation of Gases in Combustion Analysis – Gravimetric Analysis
        Pass gases through series of cartridges that selectively absorb CO2, H2O, etc. (gas-solid extraction)
        Weigh the solid cartridges before and after burning the sample.
        The difference in weight is related to the amount of gas produced and the composition of the original sample.
          P4O10 can be used to absorb H2O
          Ascarite (NaOH coated non-fibrous silicate) can be used to absorb CO2
ELEMENTAL ANALYSIS
Ascarite

## Slide 10
Chemical Methods
  Specific Elemental Methods: Carbon and Hydrogen Analysis
      II. Methods for Quantitation of Gases in Combustion Analysis – Gravimetric Analysis
        Advantages of Gravimetric Analysis
          Method is easy to perform and inexpensive
          High accuracy and precision is possible
          Sample requirement is in the mg/mg range.
        Disadvantages of Gravimetric Analysis
          Need complete combustion for good accuracy
          Must consider selectivity of the adsorption cartridges
ELEMENTAL ANALYSIS

## Slide 11
Chemical Methods
  Specific Elemental Methods: Carbon and Hydrogen Analysis
      III. Methods for Quantitation of Gases in Combustion Analysis – Gas Chromatography
        Collect gasses produced by combustion by using a cold trap or cartridge.
        Inject the mixture of gases onto a GC system to separate and quantitate individual components (e.g., CO2, H2O, NO2, SO2)
ELEMENTAL ANALYSIS
H2O
NO2
SO2
CO2
inject
Response
Retention time (min.)
Illustration of cold trap
Typical GC chromatogram

## Slide 12
Chemical Methods
  Specific Elemental Methods: Carbon and Hydrogen Analysis
      III. Methods for Quantitation of Gases in Combustion Analysis – Gas Chromatography
        Commonly used in professional labs for C/H analysis
        Advantages of GC
          Easier to perform than gravimetric analysis
          Less subject to interferences from other element.
          Sample requirement lower than gravimetric method (ng-mg)
          Can do multiple elements in a single run
        Disadvantages of GC
          More expensive than gravimetric analysis
ELEMENTAL ANALYSIS

## Slide 13
Chemical Methods
  Specific Elemental Methods: Carbon and Hydrogen Analysis
      IV. Biological Oxygen Demand (BOD)
        Measure of the total organic content of a sample (simple of complex mixtures)
          Used as a simple measure of organic pollutants in water samples
        Measure the consumption of oxygen by microorganisms added to sample
          Add microorganism
          Incubate 5 days
          Measure change in pressure of CO2 released
        Gives a measure of the total organics originally in the sample:
ELEMENTAL ANALYSIS

## Slide 14
Chemical Methods
  Specific Elemental Methods: Carbon and Hydrogen Analysis
      V. Chemical Oxygen Demand (COD)
        Measure of the total organic content of a sample (simple of complex mixtures)
        Determined by reaction of organic compounds in sample with known amount of strong oxidizing agent (potassium dichromate, K2Cr2O7)
          Remaining oxidizing agent is then titrated
          Measure the difference between final and initial amounts of oxidizing agent
        Difference in oxidizing agent is related to the total amount of organic compounds in the original sample:
ELEMENTAL ANALYSIS

## Slide 15
Chemical Methods
  Specific Elemental Methods: Nitrogen Analysis
      I. Kjeldahl Method:
        Important in the analysis of food, fertilizers, animal feeds, etc.
        A known amount of sample is first digested with boiling H2SO4 in the presence of a catalyst to convert all of the organic nitrogen to NH4+:
        Digestion:
        The solution is made basic, converting all of the NH4+ formed to NH3
        Distillation:
        The NH3 is distilled from the sample and collected into a solution containing a known excess of aqueous HCl
        Collection:
ELEMENTAL ANALYSIS

## Slide 16
Chemical Methods
  Specific Elemental Methods: Nitrogen Analysis
      I. Kjeldahl Method:
        Titrate unreacted HCL with NaOH
        This allows the amounts of NH3 that entered the solution to be determined
          Difference between known excess of HCl and remaining HCl
        Gives a measure of the organic nitrogen content of the original sample
ELEMENTAL ANALYSIS

## Slide 17
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Gravimetry
      I. Gravimetry:
        Use of a mass measurement to quantitate the amount of an analyte in a sample
          Precipitate Pb+2 with NaCl and measure the mass of the PbCl2 ppt.
        One of the earliest forms of analytical methods
          A. L. Lavoisier, 1790-Law of conservation of mass
        Can form the basis of very accurate and precise measurements
          Typical accuracy ± 0.1% relative error
          1 ppm precision
          For example, method was used by T. W. Richards, et al. to determine the atomic weights of Ag, Cl, etc. to six significant figures in the early 1900s
ELEMENTAL ANALYSIS

## Slide 18
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Gravimetry
      II. General Requirements of Gravimetric Methods:
        Requires known composition for the final product
        Assumes no other products than the one of interest
        Assumes quantitative conversion of the analyte into the final product
        Need enough final product for a mass measurements
      Ideal Properties of Products for Gravimetric Analysis:
        Insoluble
        High purity
        Easy to filter (large crystals)
        Known chemical composition
ELEMENTAL ANALYSIS
Few precipitates have all of these properties, but in most cases appropriate techniques can help optimize these qualities

## Slide 19
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Gravimetry
      IV. Process of Crystal Growth:
        Nucleation: initial stage; involves collision of molecules or ions to form small aggregates
        Particle Growth: Addition of other ions or molecules to aggregate to form a crystal
ELEMENTAL ANALYSIS
Crystal Growth

## Slide 20
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Gravimetry
      IV. Process of Crystal Growth:
        Need a saturated solution to produce precipitation
        Nucleation is faster than particle growth in highly concentrated solutions producing colloidal suspensions
        Nucleation and Particle growth always competes for molecules/ions being precipitated
          If nucleation is faster than particle growth then a large number of small aggregates occur giving a colloidal suspension
          If particle growth is faster than nucleation then only a few, large particles form giving pure crystals
ELEMENTAL ANALYSIS
Colloidal suspension
Crystal formation
Want to
Convert to

## Slide 21
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Gravimetry
      IV. Process of Crystal Growth:
        Rates of nucleation vs. particle growth depends on:
          Amount of precipitation solute present
          Described by a quantity known as the Relative Supersaturation (R)
        If R is large,
          Large relative amount of solute in solution
          Favors nucleation and colloid formation
        A small value of R (~ 1.0) is desired in order to favor crystal growth
ELEMENTAL ANALYSIS
S = Molecule or ion concentration ate equilibrium
(i.e., the solubility limit when the solution is in contact with precipitate
Q = Actual molecule or ion concentration under the given
precipitation conditions (not at equilibrium)
Colloidal Particle

## Slide 22
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Gravimetry
      V. Methods for Minimizing R:
        Increase temperature of solution
          Increases S
          Increase amount of solute that can be in solution at equilibrium
        Add precipitating reagent slowly while vigorously mixing solution
          Avoids local high concentrations of solution
          Avoids nucleation and colloid formation
        Keep volume of solution large
          Keep concentration of analyte and precipitating reagent low
        Control S by chemical means
          By adjusting pH
          By adding complexing agent, example: precipitation of Ca2+ with C2O42-
ELEMENTAL ANALYSIS
Note: As pH ([H+]) changes, the solubility of CaC2O4 changes
      C2O42- + H+ HC2O4-
      Ca2+ + C2O42- CaC2O4(s)
Ksp

## Slide 23
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Titrations
      I. Titration (Volumetric Analysis):
        Method for quantitating analyte based on measuring the volume of a reagent that is required to react with the analyte
        Also an early analytical method
          France, 1830-silver titration
        Capable of high precision,
          Accuracy can be in the range of ± 1 ppt relative error
          Favors nucleation and colloid formation

## Slide 24
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Titrations
      I. Precipitation-Based Titrations:
        Example: Titration of Ag+ with Cl-
        Monitor a change in color
Solution changes from white to brick-red as Ag+ is depleted

## Slide 25
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Titrations
      I. Redox Titrations:
        Example: Titration of Fe2+ with Ce4+
        Monitor a change in potential

## Slide 26
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Titrations
      I. Redox Titrations:
        Example: Titration of Fe2+ with Ce4+

## Slide 27
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Titrations
      I. Complexometric Titrations:
        General reaction when using EDTA as a complexing agent:
Metal – Lewis Acid or Electron-pair acceptor
Ligand – Lewis Base or Electron-pair donor
Note: multiple atoms from EDTA are binding Mn2+

## Slide 28
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Titrations
      I. Complexometric Titrations:
        EDTA (Ethylenediaminetetraacetic acid) has 6 nitrogens & oxygens in its structure giving it 6 free electron pairs that it can donate to metal ions.
          High Kf values
          6 acid-base sites in its structure

## Slide 29
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Titrations
      I. Complexometric Titrations:
        General reaction when using EDTA as a complexing agent:

## Slide 30
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Titrations
      I. Complexometric Titrations:
        EDTA reacts with most ions to form a tight, essentially irreversible 1:1 complex:

## Slide 31
General requirements of titrations:
    1. Based on solution-phase reactions (i.e., the sample must first be placed in solution before the procedure can be performed)
    2. Requires known reaction and stoichiometry between the analyte and titrant
    3. Assumes no reaction other than the one of interest occurs
    4. Reagent used as the titrant should have a large equilibrium constant and fast rate of reaction with the analyte
    5. Must be possible to make up the titrant with a known composition and purity
    6. Needs means of detecting the end of the titration
ELEMENTAL ANALYSIS

## Slide 32
ELEMENTAL ANALYSIS
Equivalence Point: the point at which the amount of titrant add is exactly equal to the amount needed to give stoichiometric consumption of the analyte
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Titrations
End Point: the point at which the amount of titrant produces an observable change during the titration, signaling the complete or near complete consumption of analyte (the actual case)
CuCl Titration with NaOH
Before any addition of NaOH
After the addition of 8 drops of NaOH
End Point

## Slide 33
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Common Methods for End Point Detection
      I. Precipitation-Based Titrations:
        Ion Selective Electrode (e.g., pH meter) for analyte, titrant or product
        Mercury Electrode set at a potential to detect analyte, titrant or product
        Visual observations or light scattering measurements
      II. Redox Titrations:
        Ion Selective Electrode (e.g., pH meter) for analyte, titrant or product
        Mercury Electrode set at a potential to detect analyte, titrant or product
        Redox Indicator:
        Complexing Agents:
starch + I3-  starch-I3- complex
(clear) (deep blue)

## Slide 34
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Common Methods for End Point Detection
      III. Complexometric Titrations:
        Ion Selective Electrode (e.g., pH meter) for analyte, titrant or product
        Mercury Electrode set at a potential to detect analyte, titrant or product
        Metal Ion Indicator:
          Use of Eriochrome black T (In) as indicator for titration of Mg+2 with EDTA

## Slide 35
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Colorimetry
      I. Colorimetry (Visible Spectrometric Analysis):
        Method for quantitating analyte based on measuring the absorbance of light by the analyte, or a species that is formed by or reacts with the analyte
          Example: Determination of Cd2+ with Hydroxyquinoline
        One of the first instrumental analytical methods
          Beckman, 1930’s
        Capable of moderate accuracy and precision,
          Limits of detection lower than titrations or gravimetry
Jour. Chem. Soc. Pak, 2001 27(5) 471

## Slide 36
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Colorimetry
      II. Process of Absorption
        Light Source Sample Detector
I
Io
where: Io = Initial intensity of light
I = Final intensity of light
%T = percent transmittance of light

## Slide 37
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Colorimetry
      III. Beer-Lambert Law (Beer’s Law):
where: e = Molar absorptivity (units, L/mol-cm)
b = Path length of light through sample (cm)
c = Concentration of absorbing species (mol/L)
A = Absorbance
= -log(I/Io)
= -log(%T/100)

## Slide 38
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Colorimetry
      IV. Assumptions behind Beer’s Law:
        All absorbing species act independently of each other
        The light being used for the absorbance measurement is “monochromatic”
        All detected rays of light that pass through the sample have the same distance of travel
        The concentration of absorbing species is constant throughout the path of light in the sample
        The light that is being used to measure the absorbance is not scattered by the sample
        The amount of light entering the sample is not large enough to cause saturation of the absorbing species in the sample

## Slide 39
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Colorimetry
      IV. Limitations of Beer’s Law – a consequence of the assumptions in Beer’s law
        Non-linearities due to intermolecular interactions
          Self-aggregation effects and electrolyte effects
        Dynamic dissociation or association of analyte
        Instrumental –Polychromatic radiation
          Different molar adsorptivities at different wavelengths leads to non-linearities in Beer’s Law
        Stray Radiation
        Mis-matched cells
          Non-zero intercept in calibration curve
In Reality:

## Slide 40
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Colorimetry
      Errors in Applying Beer’s Law to measure a concentration
        Need to keep A in range of 0.1 – 1.5 absorbance units (80 -3%T)

## Slide 41
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Colorimetry
      VI. Manual Colorimetric Measurements
        Equilibrium-Based Measurements:
          Allow reaction of analyte and reagent to reach completion
        Absorbance measurement of the final solution – endpoint measurement
        Kinetic-Based Measurements:
          Follows the consumption of analyte or reagent; or the production of the product
          Absorbance measurement as a function of time
Analytical methods 2014 6(14):10.1039/c4ay00260a
Hydrogen peroxide produced
in the glucose oxidase reaction:
2 minutes
30 minutes
5 minutes
Negative controls:

## Slide 42
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Colorimetry
      VI. Manual Colorimetric Measurements
        Photometric Titrations:
          Use of absorbance measurements to follow the progress of a titration

## Slide 43
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Colorimetry
      VI. Automated Colorimetric Measurements
        Flow-Injection Analysis (FIA):
          Injection of a sample into a system that combines the sample with one or more reagents that results in the formation of a measurable product
Flow-injection determination of chloride (a) flow diagram and (b) recorder readout for quadrupole runs on standard containing 5 to 75 ppm of chloride ion
(Ruzicka & Hansen Flow Injection Methods 2nd ed. p. 16, New York: Wiley 1988)

## Slide 44
ELEMENTAL ANALYSIS
Gravimetry, Titrations & Colorimetry
  Quantitative Elemental Analysis by Colorimetry
      VI. Automated Colorimetric Measurements
        Centrifugal Analysis:
          Use a centrifuge-type system to add, mix, and incubate sample and reagents for absorbance measurements
Coleman et al .Amer. Lab., 1971 3(7):26
Reaction mixture
after transfer
Light from
monochromator
Axis of
rotation
Removable
transfer disk
Quartz
windows
Spacer
Light to
Photomultiplier
tube
Reagent before transfer
Sample before transfer

## Slide 45
Learning Objectives
    1. Be able to define or describe each of the following methods and describe how they can be used for quantitative analysis:
    Gravimetry Colorimetry Centrifugal Analysis
    Titrations: Flow-Injection Analysis
    Precipitation-Based
    Redox
    Photometric Titration
    Complexometric (EDTA)
    2. Be able to compare and contrast the advantages and disadvantages of gravimetry, titrations and colorimetric methods. Know the general requirements of each of these methods.
    3. Be able to perform typical calculations that are involved in the use of each of the above techniques during the quantitative analysis of samples
    4. Be able to describe the ideal properties of a product in gravimetric analysis and be able to relate this to the processes involved in crystal growth
    5. Be familiar with common methods used for end point detection in precipitation-based, redox and complexometric titrations
    6. Know Beer’s Law, how it is related to the process of light absorption, and the assumptions behind this law.
ELEMENTAL ANALYSIS, GRAVIMETRY, TITRATIONS & COLORIMETRY